## Slide 1: 3D Plasma Art
University of Central Florida
Senior Design |Spring 2017
Group 20
    Monushka Sicar |Electrical Engineering
    Phillip Lane |Electrical Engineering
    Burdley Colas |Photonics Science and Engineering
    Nicolas Ramirez |Computer Engineering

## Slide 2: Motivation
Previous System:
- Made for production
- Lacking user friendliness
- Hazardous (Electrical & Optical)
- Long lead time
- Bulky in size
(a) Previous system (b) Electrical components are exposed and dangerous (b) Computer system outdated (c) Optical system to etch six glasses simultaneously, hazardous due to exposed laser beam.

## Slide 3: Goals and Objectives
- Construct to have a single glass place holder
- Improvements user friendliness
  - Automates image formatting and processing
  - Eliminates need for machine pre-orientation
- Laser automatic control
  - Automatically activates laser to start dame process
  - Turns off laser after process is completed
- Higher safety standards
  - Safeguards the PCB and the motor drivers to isolate potential electric shocks.
  - Implements a shield around the system to block reflecting laser beam.

## Slide 4: Specifications and Requirements
Optical | Laser: 1064 nm PFR 10 Hz Energy 12 mJ | Focusing lens 25.4 mm | Beam Spot Size 16 um diameter | Image Resolution 167 x 167 x 50.1 pixels | Optical Shielding
Electronics | Current source need to be 5.4 Amps | Power supply needs to be 194.4 Watts | Voltage for motors need to be 24-48 Volts per optimal performance | Move 20lbs | Safeguard Electrical components
Computer | Control Laser using RS-232 | Support USB 2.0 (12MB/s) | User friendly interface | Unification of Programs | 2D to 3D Conversion
All:
Decrease operating time by 40% (Pegasus logo)
Render different size glass
Min.Glass Size: 2 in x 2 in x 2 in
Max. project machine size: 4 ft x 4 ft x 4 ft
Notes: Controls Laser using RS-232 serial communications Start and end of Process
Decreases operating time by 40% based on standard image (Pegasus logo)
Maximum Dimension of rendered art in glass 2 inch x 2 inch x 2 inch (xyz).
Ability to have use different size glass
Must support USB 2.0 Full Speed (12 Mb/s)

## Slide 5: Responsibilities
Tasks/Names | Monushka Sicar | Phillip Lane | Nicolas Ramirez | Burdley Colas
Power | First | Second |  | 
Movement Mechanisms and Payload | Third | First | Third | Second
Commands and Control | Third | Second | First | Third
Optics |  |  |  | First

## Slide 6: Overall System Diagram
Main Supply
U.S. Standard
(110-120 VAC)
AC/DC Adaptor
(12 VDC)
Regulator
(5VDC)
Microcontroller
Stepper Motor Drivers
Stepper Motors
Motor Driver Supply
(18 - 80 VDC)
Z-Axis Mount
X and Y Surface Mount
Axis Limit Switches
USB-to-Serial Chip
Etching Glass
Optics
Movement Mechanisms and Payload
Commands and Control
Power
Laser
Optical Assembly
Monushka Sicar
Phillip Lane
Nicolas Ramirez
Burdley Colas
Phillip Lane

## Slide 7: Power
Main Supply
U.S. Standard
(110-120 VAC)
AC/DC Adaptor
(12 VDC)
Regulator
(5VDC)
Microcontroller
Stepper Motor Drivers
Stepper Motors
Motor Driver Supply
(18 - 80 VDC)
Z-Axis Mount
X and Y Surface Mount
Axis Limit Switches
USB-to-Serial Chip
Etching Glass
Optics
Movement Mechanisms and Payload
Commands and Control
Power
Laser
Optical Assembly
Monushka Sicar
Phillip Lane
Nicolas Ramirez
Phillip Lane
Burdley Colas

## Slide 8: Power
- Constraint: using laser source from old machine
- Various operating voltages
  - Laser Source: 115 VAC
  - Motor Drivers: 18-80 VDC
  - MCU: 5 VDC
 | DC Supply (Battery) | AC Supply
Erosion | High: If stayed in for too long can cause erosion | Low: No erosion occurs at power source
Circuit Damage | Low: Since it has power limitations are defined | Medium: Can occur during a power surge (Preventative measures: Surge protector)
Cost | High: Periodic Battery replacement | Low: No need to change Power supply

## Slide 9: Power Consumption (Runtime)
G201X Digital Step Drive GeckoDrive
- Voltage Rating: 18- 80 VDC
- Power Rating: 1- 13 Watts
Nema 23-Bipolar StepperOnline (340 oz-in)
- Voltage Rating: 24- 48 VDC ( Using 36 VDC)
- Current Rating: 1.8 A/ phase

## Slide 10: AC/DC Adapter
All of the electronics comprising the 3-D Laser Etching System, except the laser unit, motors, and motor drivers, are operated on direct current (DC) power
Power needs to converted to DC for the low voltage components ie. (Microcontroller), as well as provide a constant output voltage
Part Number | Input Voltage | Output Voltage | Max Output Current
120-1185 | 120 VAC | 24 VDC | 600mA
120-1165 | 120 VAC | 18 VDC | 600mA
TOL-09442 | 100 - 240 VAC | 12 VDC | 600mA

## Slide 11: Regulation
- Supplies 5 VDC to MCU
- Heat sinking a non-issue due to low current consumption
- Efficiency a non-issue due to low current output
Property | Linear | Switching
Efficiency | Low Vo/Vin | High, > 95%
Noise | Low | High, due to switching
Cost | Low | High
Regulator Type

## Slide 12: Voltage Regulation

## Slide 13: Commands and Control
Main Supply
U.S. Standard
(110-120 VAC)
AC/DC Adaptor
(12 VDC)
Regulator
(5VDC)
Microcontroller
Stepper Motor Drivers
Stepper Motors
Motor Driver Supply
(18 - 80 VDC)
Z-Axis Mount
X and Y Surface Mount
Axis Limit Switches
USB-to-Serial Chip
Etching Glass
Optics
Movement Mechanisms and Payload
Commands and Control
Power
Laser
Optical Assembly
Monushka Sicar
Phillip Lane
Nicolas Ramirez
Phillip Lane
Burdley Colas

## Slide 14: Commands and Control
Main Supply
U.S. Standard
(110-120 VAC)
AC/DC Adaptor
(12 VDC)
Regulator
(5VDC)
Microcontroller
Stepper Motor Drivers
Stepper Motors
Motor Driver Supply
(18 - 80 VDC)
Z-Axis Mount
X and Y Surface Mount
Axis Limit Switches
USB-to-Serial Chip
Etching Glass
Optics
Movement Mechanisms and Payload
Commands and Control
Power
Laser
Optical Assembly
Monushka Sicar
Phillip Lane
Nicolas Ramirez
Phillip Lane
Burdley Colas

## Slide 15: UART Chip Selection
Selection Criteria
- Pre-programmed
- Support USB 2.0 Full Speed (12 Mb/s)
- 5 V Operation
- Cost
Characteristic | FTDI FT232RL | Microchip PIC18F2550 | Maxim MAX3100
Pre-programmed | Yes | No | No
Support Speed (Mb/s) | 12 | 12 | 12
Operating Voltage (V) | 4 - 5.25 | 2 - 5.5 | 2.7 - 5.5
Cost (USD) | 4.75 | 4.13 | 5.23

## Slide 16: FT232 IC
Purpose
- USB-to-Serial Conversion
  - Programming MCU
  - Gcode streaming

## Slide 17: Commands and Control
Main Supply
U.S. Standard
(110-120 VAC)
AC/DC Adaptor
(12 VDC)
Regulator
(5VDC)
Microcontroller
Stepper Motor Drivers
Stepper Motors
Motor Driver Supply
(18 - 80 VDC)
Z-Axis Mount
X and Y Surface Mount
Axis Limit Switches
USB-to-Serial Chip
Etching Glass
Optics
Movement Mechanisms and Payload
Commands and Control
Power
Laser
Optical Assembly
Monushka Sicar
Phillip Lane
Nicolas Ramirez
Phillip Lane
Burdley Colas

## Slide 18: MCU Selection
Selection Criteria
- UART communication
- ≥ 9 Digital I/O Pins (3 PWM)
- Cost/Component Form
- Current consumption
- Speed
- 5 V Operation
Characteristic | Atmel ATmega 328P | Atmel ATmega 32U4 | Atmel ATmega 2560
Operating Voltage | 1.8 - 5.5 V | 2.7 - 5.5 V | 1.8 - 5.5 V
Serial Port (UART) | Yes, one port | Yes, one port | Yes, four ports
Flash Memory | 32 KB | 32 KB | 256 KB
Max I/O pins | 14 (6 PWM) | 20 (7 PWM) | 54 (15 PWM)
Max Frequency (at 5 V) | 20 MHz | 16 MHz | 16 MHz
Current (max frequency) | ~ 12 mA | ~ 13 mA | ~ 20 mA
Cost / Form | $4.30 / TH | $6.95 / SMD | $4.95 / SM)

## Slide 19: MCU Schematic

## Slide 20: MCU Communication

## Slide 21: MCU Firmware

## Slide 22: MCU Firmware
Critical System Needs
- Concurrent control of 3 stepper motors
- Acceleration management
  - Lines
  - Corners
  Arcs
- Automatic Homing
- Look Ahead Planning
- Storage of travel settings
  - Steps/millimeter
  - Max Speed and Acceleration
Teacup

## Slide 23: Firmware Options
Feature | Firmware |  | 
 | GRBL | Marlin | Teacup
Homing | Yes | Yes | Yes
Acceleration Management | Yes | Yes | Yes
Concurrent Motor Control | Yes, 3 motors | Yes, 3 motors | Yes, 4 motors
Look Ahead Planning | Yes | Yes | Yes
Travel Settings Storage | Yes | Yes | Yes, optional

## Slide 24: Grbl High Level Diagram
Start
Homing
GCode Buffer
Read Command
Parse Command
Velocity & Acceleration Planner
Buffer Full?
Execute Command
NO
YES
Wait for Command to Clear
Clear Command
Accept Command
Command Cleared

## Slide 25: Commands and Control
Main Supply
U.S. Standard
(110-120 VAC)
AC/DC Adaptor
(12 VDC)
Regulator
(5VDC)
Microcontroller
Stepper Motor Drivers
Stepper Motors
Motor Driver Supply
(18 - 80 VDC)
Z-Axis Mount
X and Y Surface Mount
Axis Limit Switches
USB-to-Serial Chip
Etching Glass
Optics
Movement Mechanisms and Payload
Commands and Control
Power
Laser
Optical Assembly
Monushka Sicar
Phillip Lane
Nicolas Ramirez
Phillip Lane
Burdley Colas

## Slide 26: Axis Limit Switches
Velleman’s Lever Switch
- NO or NC
- Two holes for mounting
- Lever best pushed by inclined contacts
Radioshack’s Push Button Switch
- NO only
- Can insert in 1/4” holes
- Pushed by direct linear contact/force

## Slide 27: Overall Schematic
Regulated 5 V
MCU Power
GCODE Interpretation and Motor Control
Data Streaming via UART

## Slide 28: Commands and Control
Main Supply
U.S. Standard
(110-120 VAC)
AC/DC Adaptor
(12 VDC)
Regulator
(5VDC)
Microcontroller
Stepper Motor Drivers
Stepper Motors
Motor Driver Supply
(18 - 80 VDC)
Z-Axis Mount
X and Y Surface Mount
Axis Limit Switches
USB-to-Serial Chip
Etching Glass
Optics
Movement Mechanisms and Payload
Commands and Control
Power
Laser
Optical Assembly
Monushka Sicar
Phillip Lane
Nicolas Ramirez
Phillip Lane
Burdley Colas

## Slide 29: Software Design
Programming Language
Python
  - Python vs Java
  - Time Efficiency
  - Extensive Standard Library
Libraries
- TkInter
- pySerial
- Pillow
Operating System
- Windows 10

## Slide 30: Simplified Flow
User Input
2D - 3D Conversion
Etching

## Slide 31: 2D to 3D Conversion

## Slide 32: Example Conversion
JPG/PNG File BMP SVG STL

## Slide 33: Gcode Creation
G-code
- Numerical Control Language
- Standard in CAM tools and machines
- Movements
  - Where to, how fast, what path
Slicing
- Slic3r
- 3D object is “cut” into horizontal slices
- Each slice is converted into Gcode
- Layered Toolpaths
Example G-code

## Slide 34: Gcode Streaming
Python Script
- Pyserial module
- Python Standard Library
RS-232 Interface
- Serial communications interface
- Laser control before and after streaming
USB
- Microcontroller communications
- Gcode transmission

## Slide 35: User Interface
TkInter Module
- Python Standard Library
- Layer over Tcl/Tk Toolkit
- Object Oriented
Major Focuses of UI
- Automation
- Simplicity
- Unification

## Slide 36: User Interface Design

## Slide 37: Optics
Main Supply
U.S. Standard
(110-120 VAC)
AC/DC Adaptor
(12 VDC)
Regulator
(5VDC)
Microcontroller
Stepper Motor Drivers
Stepper Motors
Motor Driver Supply
(18 - 80 VDC)
Z-Axis Mount
X and Y Surface Mount
Axis Limit Switches
USB-to-Serial Chip
Etching Glass
Optics
Movement Mechanisms and Payload
Commands and Control
Power
Laser
Optical Assembly
Monushka Sicar
Phillip Lane
Nicolas Ramirez
Phillip Lane
Burdley Colas

## Slide 38: Optical System Design
Changes in Design to meet Customer needs:
- These two previous designs were replaced to have the beam propagates on a straight axis.
- Change in axis of propagation leads to optical power loss and polarization change.
- Change of the optical design yields to smaller size system.
- Optical elements on these designs are for the wavelength 532 nm.
1
2

## Slide 39: Optical System Design
Legend:
- Optical system is assembled along the Z-Axis
- Iris serves as an aperture in front of the laser
- Polarizer and Half Wave Plate serves as an analyzer controlling the laser beam energy before damaging the glass
- Focusing lens is a plano convex lens

## Slide 40: Laser:
- Type: Nd-YAG
- Operating Wavelength: 1064 nm
- Energy: 10 mJ
- PRF: 5 Hz
- Pulse Width: 10 ns
- Q-Switched
- Pulsed
- Water Cooled
- Flashlamp Pumped
Laser Operation:
Turn Key
Adjust Desired Energy level
Adjust Repetition Rate Frequency
Push Q-Switch
FIRE/STOP (control through RS-232)
Credit: Big Sky Laser Manual

## Slide 41: Laser
Laser spectrum
Energy Level vs Output Energy Measured
Parameters:
- Laser was not able to operate at 532 nm due to fault of the nonlinear crystal.
- Laser stability is questionable. Beam Profile is not an evenly distributed.
Laser Beam wonders due to the nonlinear crystal.
Note: Calibration of laser would yield to accurate measurements yielding to better image resolution.

## Slide 42: Focusing Lens
Determining the Focal Spot size of the Laser Beam at the Glass:
𝛌 = 1064 nm d = (2w) = 1.3 mm s = 1054.792 mm
Fl = 25.4 mm p = 500 mm s”= 25.996 mm
M2 = 1 d0= (2w0) = 0.677 mm d0” = 0.016 mm
𝛳 = 1 mRad z = 554.792 mm zr” = 0.186 mm
Credit: http://www.ophiropt.com/laser-measurement-instruments/laser-power-energy-meters/services/focal-spot-size-calculator-for-gaussian-beams

## Slide 43: Image Resolution:
- Our Image to etch is the
UCF Pegasus Logo
- Dimension
1 inch x 1 inch x 0.3 inch
- Resolution
167 x 167 x 50.1 pixels
- Beam spot size
16 um diameter
- Thickness Layer Spacing
1 mm

## Slide 44: Administrative Content

## Slide 45: Project Budget
Notes: Monushka : Burdley & Nick, can you insert your last purchase on the Overall project budget
All: Once burdley & nick insert theirs , I will add it to this slide

## Slide 46: Acknowledgement
This project is sponsored by Dr. M.J. Soileau from The College of Optics and Photonics, CREOL.

## Slide 47: Questions?